## Slide 1
HYDROWEB a operational Satellite Altimetry Database
for Rivers and Lakes
P. Maisongrande (CNES/LEGOS)
on behalf of
J.-F. Crétaux (CNES/LEGOS), S. Calmant (IRD/LEGOS), J. Dorandeu (CLS)

## Slide 2: a solution for the Global Runoff Inventory
Only dark blue points are now available
Avalaible time series of water levels
for rivers and lake from 1992 to 2018
(ERS-1, Topex/Poseidon, ERS-2, GFO), Jason-1 , Envisat, Jason-2 Altika, S3…...)
Satellite Altimetry
HYDROWEB why and how?

## Slide 3: HYDROWEB.Theia-Land.fr
Developed by LEGOS, maintained & operated by CLS (since 2016) under CNES & Copernicus contracts
Rivers | 1490
Operational | 260
Research | 1290
Lakes | 155
Operational | 64
Research | 91
Operational: calculated and released automatically (1day latency)
Research: longer latency ( ~months) adjusted (small water bodies, signal analysis, artifacts…)
Frequent water levels for rivers & lakes

## Slide 4: HYDROWEB.Theia-Land.fr Examples
Lake Toktogul

## Slide 5: HYDROWEB.Theia-Land.fr Examples
Lake Toktogul

## Slide 6: HYDROWEB.Theia-Land.fr Examples
Toktogul lake

## Slide 7: HYDROWEB.Theia-Land.fr Examples
Lake Toktogul

## Slide 8: HYDROWEB.Theia-Land.fr Examples

## Slide 9: HYDROWEB.Theia-Land.fr
Kainji lake & Niger River

## Slide 10
Creation of rating curves using the MGB model estimates of river discharge
New product
A priori information for SWOT
Floodplains water level, extent and volume changes
Inner Niger Delta Combination of water level from satellite altimetry & water extent from satellite imagery.
River discharge over more than 1000 virtual stations
HYDROWEB Futur Products (by 2019)
Rating curves
Watel level (m)
Discharge (m3/s)

## Slide 11
2021: SWOT arrival in HYDOWEB
  Provide a global inventory of all terrestrial water bodies whose surface area exceeds (250m)2 (lakes, reservoirs, wetlands) and rivers whose width exceeds 100 m (rivers).
  Water levels of lakes, rivers and wetlands with a vertical accuracy of few cm for lakes and 10 cm over 1km² for rivers;
  Measurement of the global storage change in fresh water bodies at sub-monthly, seasonal, and annual time scales.
  Estimation the global change in river discharge at sub-monthly, seasonal, and annual time scales.
  Observations of estuaries
Surface Water and Ocean Topography
Notes: Parler de revisiting capacity

## Slide 12: Altimetry revisiting capacity
Sentinel- 3A (1every 27 days)
Sentinel- 3B (1 every 27 days)
Jason-3 (1 every 10 days)
~50 km de Diama
~95 km de Diama

## Slide 13: SWOT revisiting capacity
~50 km de Diama
~95 km de Diama
2 obs. SWOT par période de revisite (21j)
1 obs. SWOT /21 days

## Slide 14: HYDROWEB.Theia-Land.fr
Summary
An operational data base at
An embedded database Hydroweb<Theia<Copernicus<others
An increasing number of Stations (eg S3 in progress)
Linkage with in situ data, an infrastructure challenge
From water level to added value products: volume and discharge
HYDROWEB prepares the arrival of SWOT in 2021

## Slide 15: HYDROWEB.Theia-Land.fr
Thank you
Contact : Jean-François.Crétaux@legos.obs-mip.fr

## Slide 16
HYDROWEB a operational Satellite Altimetry Database
for Rivers and Lakes
P. Maisongrande (CNES/LEGOS)
on behalf of
J.-F. Crétaux (CNES/LEGOS), S. Calmant (IRD/LEGOS), J. Dorandeu (CLS)